DFL-870

Date: 2016/11/9

| Product Name: | DFL-870 Network Security UTM Firewall |
| --- | --- |
| Revision: | A1 |
| Availability: | Nov, 2016 |
| Picture: |  |
| Why Sell This Product: | DFL-870 is D-Link next generation UTM firewall. It is easy-to-deployed and designed for medium business, school, and government organizations that require superior price/performance. This device is a powerful security solution that provided integrated Firewall, Intrusion Prevention System(IPS), Anti-Virus, Load Balance, Fault-Tolerance, Zone-Defense, Web Content Filtering, User Authentication, Denial of Service (DoS) protection as well as Virtual Private Network (VPN) support. Selling Points All-in one UTM firewall/VPN/network security functions. Good Firewall/VPN/UTM performance D-Link ZoneDefend End-Point security 6 configurable gigabit Ethernet ports to provide flexible usage. Dual WAN ports provide WAN failover and load balancing Link Aggregation |
| Key Features: | Performance Overview: 6 x 10/100/1000Mbps configurable Ethernet ports 4Gbps plaintext firewall throughput 1Gbps 3DES/AES VPN throughput 450 Mbps IPS/IDP Throughput 600 Mbps Antivirus Throughput 700 Mbps Application Throughput Concurrent session: 500,000 VPN Tunnel: 200 |
| Technical Details: | Integrated Firewall Multiple WAN Ports WAN Failover, Outbound Load Balancing Link Aggregation IEEE 802.1q VLAN Granular Bandwidth Management D-Link End-to-End Security Solutions (E2ES) Integration with Proactive D-Link ZoneDefense™ Unified Threat Management (UTM) Intrusion Prevention System (IPS) Antivirus (AV) Protection Web Content Filtering (WCF) in HTTP/HTTPS Application Control E-mail Security Virtual Private Network (VPN) IPSec/PPTP/L2TP/SSL/GRE Redundant VPN Gateway Hub and Spoke Advanced Functions User Authentication Web-based HTTP/HTTPs Authentication (Captive Portal) User Identity Awareness Active-Passive High Availability Logging and Monitoring Internal log capacity: 500 records Log viewer Email notification Support external log server: syslog server Support 8 log receivers Real-Time performance monitor Event log and alarm Sorting/Filtering/Search log messages Support SNMP v1, v2c SNMP Trap SNMP Standard MIB-II and Private MIB VPN tunnel monitor |
| EMI/EMC Report | ( FCC No. ( CE No. ( VCCI No. ( CTR-21 No. ( RCM No. ( A-Tick No. ( FDA No. ( R&TTE No. ` ( BSMI No. ( IC No ( Others: EAC |
| Safety | ( TUV No. ( UL No. ( CSA No. ( CB No. ( CE ( Others: |
| Packaging Style | (Clamshell ( White Box (Gift Box Bulk (Brown Box (Others |
| Packaging Contents: | DFL-870 x 1 CAT5 Ethernet cable x 1 QIG x1 Power Cord x 1 Mini-USB to RJ45 Console cable x 1 Rack Mounting Bracket x2 |
| Country of Origin: | China |
| UPC Code: | 790069 429293 RFL870A1A....A1G |
| Units Per Carton: | For USA | For EU | For WW |
|  | 4 pcs/Carton | 4 pcs/Carton | 4 pcs/Carton |
| Cartons Per Pallet: | For USA | For EU | For WW |
|  | (Air): pcs (Sea): pcs No USA request | (Air): pcs (Sea): pcs No EU request | (Air): 27 pcs (Sea): 36 pcs |
| Dimensions and Weight: | Box Dimensions:  237x168x36mm (Type A)  168x237x53mm (Type A53)  225x150x75mm (Type B)  150x225x55mm (Type B1)  269x162x65mm (Type C)  274x208x68mm (Type D)  208x274x95mm(Type D95)  208x137x95m (T pe D95 half)  274x208x118mm (Type D1)  274x208x138mm (Type 2)  208x274x190mm (Type D4)  288x245x66mm (Type E)  245x285x82mm(Type E1)  245x285x87mm(Type E2)  256x356x97mm (Type F)  137x208x36mm (Type G)  208x250x68mm (Type H)  253x27x24 mm (Type I) ( Others: 396 x 273 x 80 mm Device (mm/g): Device Length Device Width Device Height Device Weight 278 mm 183 mm 44 mm 1700 Carton (cm/kg): Carton Length Carton Width Carton Height Carton Gross Weight 35.0 29.2 41.8 12.1 kg Pallet (cm/kg) for DEU Carton per Air Pallet Air Pallet PCS Air Pallet Length Air Pallet Width Air Pallet Height Air Pallet Weight 27 108 110 120 140 325.0000 Carton per Sea Pallet Sea Pallet PCS Sea Pallet Length Sea Pallet Width Sea Pallet Height Sea Pallet Weight 36 144 110 120 140 433.9000 Pallet (cm/kg) for DI Carton per Air Pallet Air Pallet PCS Air Pallet Length Air Pallet Width Air Pallet Height Air Pallet Weight 27 108 110 120 140 325.0000 Carton per Sea Pallet Sea Pallet PCS Sea Pallet Length Sea Pallet Width Sea Pallet Height Sea Pallet Weight 36 144 110 120 140 433.9000 Intrastat Weight(kg) Full Package Weight Net Mass Weight (WEEE Weight) Packaging Weight- Paper Packaging Weight- Plastic Packaging Weight- Mixed SubTotal Weight Paper+Plastic+Mixed 2.6700 2.1078 0.5500 0.0120 0.0002 0.5622 |