Q1.  Can the Physical Port and Network Port options be used at the same time?  If yes, which one takes precedence and how do they interact with each other?

Ans:  Yes, they can be used to work at the same time. Because Physical Port function's main behavior is LAN client uploads LAN server. But Network Port function's main behavior is LAN client uploads WAN server. The two functions don't interact with each other.

Q2.  How does the router handle the three priority levels?  If Low, Normal, and High priority traffic is being transferred through the router at the same time, will the router pass all High Priority packets first then transfer the Normal, and finally transfer the Low priority ones?  Or will the router alternate between High, Normal, and Low in a round robin type fashion?

Ans:  DI-804HV will pass all High Priority packets first then transfer the Normal, and finally transfer the Low priority ones.

If you need more information, please refer to attached file.

Q3.  Will QoS apply to traffic going over VPN tunnels?

Ans:  No, we don't support this application at present.