VPN L2TP Application

Installation Guide

Configuring a Remote Access L2TP VPN Dial-in Connection

A remote worker establishes a L2TP VPN connection with the head office using Microsoft's VPN Adapter (included with Windows XP/2000/ME, etc.). The router is installed in the head office, connected to a couple of PCs and Servers.

Configuring L2TP VPN in the Office

The input IP address 192.168.1.200 will be assigned to the remote worker. Please make sure this IP is not used in the Office LAN.

| Item | Function | Description |
| --- | --- | --- |
| 1 | Connection Name | YUJI_test | Given a name of L2TP connection |
| 2 | Dial in |  | Check Dial in |
|  | Private IP Address Assigned to Dialing User | 192.168.15.199 | An assigned IP address for the remote worker |
| 3 | Username | yuji | Input username & password to authenticate remote worker |
|  | Password | 123456 |  |
| 4 | Auth.Type | Chap(Auto) | Keep as default value in most of the cases. |
| 5 | Idle Timeout | 0 | The connection will be disconnected when there Is no traffic in a predefined period of time. Idle time 0 means the connection is always-on. |
| 6 | IPSec |  | Enable for enhancing your L2TP VPN security. |
|  | Authentication | MD5 | Both sites should use the same value. |
|  | Encryption | 3DES |  |
|  | Perfect Forward Secrecy | None |  |
|  | Pre-shared Key | 12345678 |  |

Configuring Remote Worker for Dial-out to the Router

| Step 1 Select “New Connection Wizard” to create a VPN-L2TP dial out service. |  |
| --- | --- |
| Step 2 Click Next > to the next step. |  |
| Step 3 Check “Connect to the network at my workplace” radio button. Click Next > to the next step. |  |
| Step 4 Check “Virtual Private Network connection” radio button. Click Next > to the next step. |  |
| Step 5 Give a name to the L2TP connection. Click Next > to the next step. |  |
| Step 6 Input VPN-L2TP Server’s IP address. You can use Host name, only if the DDNS function is enabled in the Router. Refer to the user manual for more detail. Click Next > to the next step. |  |
| Step 7 Click Finish to the next step. |  |
| Step 8 Open Network Connections and double click on the VPN L2TP icon. |  |
| Step 9 Select “Networking” tab, and change “Type of VPN” to “L2TP IPSec VPN”. |  |
| Step 10 Select “Security” tab. Click IPSec Settings… to the next step. |  |
| Step 11 Input pre-shared key. Note: This pre-shared key must be identical as set up in the Router. Click OK to the next step. |  |
| Step 12 Click OK to continue. |  |
| Step 13 User name and Password should be identical as set up in Router. (See Item 3) Click Connect to establish a connection to your VPN-L2TP Server. Completed! |  |

# Text boxes

3

Dial-in

5

4

2

1

6